## Slide 1: IoT Edge Session
Pied Piper Program
2nd August 2017
Alberto Ramos
@AlbertoSyd

## Slide 2: Prerequisites
Raspberry Pi 3 B with 16GB SD card (Raspbian Jessie)
  Follow the Raspberry Pi setup procedure
Install Virtualbox and Vagrant
Notes: Mention the Digital and IT Transformation: Modernize, AUTOMATE, Transform

## Slide 3: Agenda
IoT Concepts
Sensors and Actuators
External Communications
From Prototyping to Final Product
Notes: Mention the Digital and IT Transformation: Modernize, AUTOMATE, Transform

## Slide 4: Fast Forward into the Future
https://www.youtube.com/watch?v=OFzSa8oW5WA

## Slide 5: IoT Concepts

## Slide 6: IoT Concepts
Sensors
  Inputs into the system
Actuators
  Outputs of the system
IOT Device (Microcontroller)
  Sensors/actuators don’t work by alone
Gateway
  Aggregates, analyses, cleanses data
  Real-time decision making
  Sends meaningful data. Lower transfer cost

## Slide 7: CPU vs MCU vs FPGA
Microprocessor
  Contains only CPU. Relies on external peripherals: ROM, RAM, disks …
  Deal with Complex tasks. General purpose
  Intel, AMD, Qualcomm, Broadcom, NVDIA, IBM, … X86, ARM architectures
Microcontroller
  Contain processor (single core), RAM, ROM and I/O pins in the chip. No OS
  Used in embedded systems. Compact format. Cheaper
  Firmware (vs OS). Deal with specialised tasks
  Texas Instruments, Microchip, … Atmel, Espressif
FPGA (Field Programmable Gate Arrays)
  Use HDL (Hardware Description Language) to configure internal circuitry
Notes: Microcontrollers run their code from ROM whereas Microprocessors run only the boot code from ROM. Then they load the code in RAM during the boot process and run it from there.

## Slide 8: SBC vs Development Board
Single Board Computer
  Full-blown computer with everything required on the board
  Lower specifications than full scale computers
  Raspberry PI, Beaglebone Black, C.H.I.P, Intel Edison, Orange PI, Banana PI
Development Board
  Contains microcontroller, power supply, crystal, female headers, USB, …
  Typically used for prototyping
  Arduinos, NodeMCU, Photon, Teensy, Feather, Lilypad …
  Often can be programmed through an IDE, ex: Arduino IDE
Notes: http://makezine.com/comparison/boards/

## Slide 9: Elements of Microcontrollers
CPU (ex: Atmega328P 8-bit in Arduino)
Clock (8MHz – 50MHz as opposed to GHz)
RAM, ROM, Flash memory - Usually in the KB range
Logic Level – 5V vs 3.3V
Digital ports – 0 or 1
Analog ports
  ADC
  Resolution depends on internal ADC, ex: 10bit = 0-1023
Notes: https://store.arduino.cc/usa/arduino-uno-rev3
https://learn.sparkfun.com/tutorials/logic-levels
https://learn.sparkfun.com/tutorials/analog-to-digital-conversion

## Slide 10: Elements of Microcontrollers
PWM – Pulse Wave Modulation
  Use digital signal to represent analog
  Frequency is important for each application
  Typically deal with it through a library
  Ex: Dimming LEDs, Servo angle, Motor speed
Serial
  No clock = Async = Baud rate, data bits, sync bits …
  Half/Full Duplex, Simplex (ex: LCD)
  Managed by UART chip, typically inside the MCU
  Used with Bluetooth, GPS … flashing firmware, serial monitor
  Careful not to connect more than 1 device at once
Interrupts
  Interrupt Service Routine gets attached to a pin
  When triggered, the processor saves execution state, runs ISR and resumes
Notes: https://learn.sparkfun.com/tutorials/pulse-width-modulation
https://learn.sparkfun.com/tutorials/serial-communication/serial-intro
If a microcontroller doesn’t have a UART (or doesn’t have enough), the serial interface can be bit-banged - directly controlled by the processor. This is the approach Arduino libraries like SoftwareSerial take. Bit-banging is processor-intensive, and not usually as precise as a UART, but it works in a pinch!
https://www.arduino.cc/en/Reference/SoftwareSerial

## Slide 11: Elements of Microcontrollers
SPI (Serial Peripheral Interface)
  One master (typically MCU) to multiple slaves
  Programmed through a library
Pros
  Synchronous. Clock signal from the Master
  Faster, ex: 10 Mbits/sec
  Simpler. Cheaper hardware
  No baud rate mismatches. No extra bits overhead
Cons
  4 Pin required (SCK, MOSI, MISO, SS= Slave Select)
  1 additional SS Pin for each new slave
    Can share one pin if only output required, ex: LEDs
Notes: https://learn.sparkfun.com/tutorials/i2c
https://learn.sparkfun.com/tutorials/serial-peripheral-interface-spi
https://learn.sparkfun.com/tutorials/raspberry-pi-spi-and-i2c-tutorial

## Slide 12: Elements of Microcontrollers
I2C (Inter Integrated Circuit)
Multiple slave IC’s communicate with one or more Master IC’s
Up to 1008 slave devices
Simpler hardware than Serial
Commonly up to 400KHz
Requires 2 pins: SDA and SCL
Notes: https://learn.sparkfun.com/tutorials/i2c
https://learn.sparkfun.com/tutorials/serial-peripheral-interface-spi
https://learn.sparkfun.com/tutorials/raspberry-pi-spi-and-i2c-tutorial

## Slide 13: Sample Microcontroller Specs – Arduino Mega
Notes: https://store.arduino.cc/usa/arduino-mega-2560-rev3

## Slide 14: Raspberry PI GPIO
General Purpose Input/Output
  3.3V logic level. No 5V tolerant
  26 digital pins. No analog
  Can reconfigure almost all GPIO pins:
    SPI, PWM, I2C, Interrupt
Code in many languages
Python - RPi.GPIO module:
  Installed in Raspbian by default
  Scripts must be run as root
Also available for Python:
  Pigpio (daemon, 32 PWM pins)
  RPIO
  WiringPi2-Python
  gpiozero
Notes: https://learn.sparkfun.com/tutorials/raspberry-gpio/gpio-pinout
http://elinux.org/RPi_GPIO_Code_Samples (C#, Python, Ruby, Perl, Basic, Shell, Java, Scratch, Pascal, …)
http://elinux.org/RPi_Low-level_peripherals
http://elinux.org/RPi_BCM2835_GPIOs

## Slide 15: Raspberry PI GPIO
Many PIN numbering conventions
  Physical numbering
  GPIO numbering
Notes: https://learn.sparkfun.com/tutorials/raspberry-gpio/gpio-pinout
http://abyz.co.uk/rpi/pigpio/python.html
https://learn.sparkfun.com/tutorials/raspberry-pi-spi-and-i2c-tutorial

## Slide 16: Raspberry PI GPIO
To complete ??????
Notes: https://learn.sparkfun.com/tutorials/raspberry-gpio/gpio-pinout
https://www.raspberrypi.org/documentation/hardware/raspberrypi/README.md
https://learn.sparkfun.com/tutorials/raspberry-pi-spi-and-i2c-tutorial

## Slide 17: Basic Electricity
Ohm’s Law
Multimeter
Electricity flows from High Voltage to Low Voltage
  from VCC to GND

## Slide 18: Breadboard

## Slide 19: Lab 1: IoT Hello World

## Slide 20: Blink an LED
Clone repo:
  https://github.com/cermegno/iot-rpi
Patch the Raspberry Pi as follows:
    - 15
    + 1
    N unpatched

## Slide 21: Blink an LED
Examine “led1.py” script with IDLE. Run it by pressing F5
This works … but it is not best practice
  Use variables at the top to define what each pins function is
  Follow in Python the same structure as with MCU’s
  Detect CTRL-C and execute GPIO.cleanup() on exit
Examine “led2.py” and run it
Exercise: Can you get it to do 5 fast flashes and a pause?

## Slide 22: Blink an LED – the Arduino way

## Slide 23: Sensors and Actuators

## Slide 24: Sensors vs Shields or HATs
Sensors/Actuators can be packaged:
By themselves
On a small board along with any components required, ex: resistors
Included into a board that can be stacked atop Arduino, Raspberry PI
  Arduino Shields
  RPi HAT (Hardware Added on Top)

## Slide 25: Sensor examples
Basics: LED, Strip, Displays, Buttons, Potentiometer, Buzzer, Joystick
Environmental: Temperature, Humidity, Brightness, UV, Colour, Barometric, Hygrometer, Sound/Noise, Liquid Level, Liquid Flow, Geiger
Gas: CO2, CO, Methane, Propane, Ethanol …
Motion: Accelerometer, Magnetometer, Hall Effect, Motion, Flex, Force, Ultrasonic, Vibration, Laser or IR Tripwire, GPS, Lidar
DC Motor, Servo, Stepper Motor, Relay, Linear Actuator
SD Card, RFID, Infrared, RF, Bluetooth, Cellular, XBee …
Notes: https://learn.sparkfun.com/tutorials/lidar-lite-v3-hookup-guide
https://newsroom.cisco.com/feature-content?type=webcontent&articleId=1360403

## Slide 26: HAT and Shield Examples
Motor Controller
PWM/Servo
TFT Display, LED Matrix, eInk
Prototyping, Expansion shield
Check Pimoroni website for more HAT ideas
Notes: https://learn.sparkfun.com/tutorials/arduino-shields

## Slide 27: Lab 2: Sensor Example

## Slide 28: Lab 2: Measuring Light
Let’s use a photoresistor to read light levels
Photoresistor (analog)  ADC  RPi
Patch as in page 59 of the manual
  CS 11
  DATA 12
  CLK 13
Don’t forget to patch 5V and GND to the
buses (the 2 small cables in the diagram)

## Slide 29: Lab 2: Measuring Light
Open a terminal on your Raspberry Pi and run the following
  sudo python photoresistor.py
You can get the ADC0832 module from here
https://github.com/sunfounder/Sunfounder_UltraKit_Python_Code_for_RaspberryPi/blob/master/ADC0832.py
wget https://goo.gl/vMNKCM
It gets downloaded with that name. Rename it: mv vMNKCM ADC0832.py
Cover the photoresistor. Can you see the readings change?
Any ideas?
Notes: If you use the –O option with wget you can specify the name of the output file
wget -O ADC0832.py https://goo.gl/vMNKCM
This is the real repo from Adeept
https://github.com/adeept/Starter_Kit_Python_Code_for_RPi
You might have to tweak the pin definition in the ADC script

## Slide 30: External Communications

## Slide 31: External Communications
In most cases we need to get the data out of the edge
Need specific simpler protocols because of processing limitations of MCU
  Easier on a SBC like Raspberry Pi
Many protocols
  (Short-range) ZigBee (industrial), Zwave and Thread (home automation), BLE …
  (Long-range, low power, low bandwidth) LoRaWAN, Sigfox, Neul …
  Wifi, Cellular
Pull (Ex: Web server)
Push (Ex: Message Queuing like MQTT)
Notes: https://www.rs-online.com/designspark/eleven-internet-of-things-iot-protocols-you-need-to-know-about
https://www.postscapes.com/internet-of-things-protocols/

## Slide 32: MQTT – Message Queuing for Telemetry Transport
Designed by Andy Stanford-Clark (IBM) and Arlen Nipper in 1999
The MQTT protocol enables a publish/subscribe messaging model
  Very lightweight (small code footprint and small network bandwidth)
Mosquitto is an Open Source MQTT v3.1 broker
Clients connect to a broker and/or:
  Subscribe to ‘topics’
  Publish messages to ‘topics’
Topics are a hierarchy with “/” as separator, ex: meals/lunch/steak
  Two wildcards: + (single level), # (all remaining levels)
    a/b/c/d matches a/+/c/d and a/+/c/+
    a/b/c/d matches a/# and a/b/#
Notes: Andy Standford-Clark TED talk https://youtu.be/s9nrm8q5eGg
https://mosquitto.org
https://pypi.python.org/pypi/paho-mqtt/1.3.0
http://www.steves-internet-guide.com/client-objects-python-mqtt/
http://www.steves-internet-guide.com/mqtt-python-callbacks/
https://www.digitalocean.com/community/tutorials/how-to-install-and-secure-the-mosquitto-mqtt-messaging-broker-on-centos-7
http://www.hivemq.com/mqtt-essentials/

## Slide 33: Lab 3: Flask Web Server

## Slide 34: Lab 3: Flask Web Server in Raspberry Pi
For a small number of edge devices you can read values when required
Let’s make a web page with the thermistor readings … with Flask of course
Open a terminal to the Rasberry Pi and run:
  sudo python photo-flask.py
Open a browser and point it to the IP of your Raspberry Pi
Move the sensor to change the readings and refresh the browser
QUESTION: How could you turn on the LED remotely?
Notes: http://mattrichardson.com/Raspberry-Pi-Flask/index.html

## Slide 35: Lab 4: MQTT

## Slide 36: Lab 4: MQTT
This is the full end-to-end scenario
RasPi
MQTT pub
Photoresistor
Mosquitto
Broker
Flask
Webpage
Redis
Python
MQTT sub
LAPTOP

## Slide 37: Lab 4: MQTT – VM steps
Use Vagrant to bring up the environment (use WIFI first, then tethering?)
  vagrant up
Log in as “vagrant”. Verify Redis is running
  ps –fe | grep –i redis
  sudo service redis status
Verify Flask works and can read Redis. Verify with your browser
  sudo python get-redis-value.py
Verify Mosquitto is running
  ps -ef | grep -i mosquito
  sudo service mosquitto status

## Slide 38: Lab 4: MQTT – VM steps
Verify Mosquitto works – mosquito clients
  Open 2 Putty terminals to the Vagrant VM. Run each line on one
  mosquitto_sub -h 127.0.0.1 -t test
  mosquitto_pub -h 127.0.0.1 -t test -m "Hello world"
Verify Mosquitto works with Python paho-mqtt library
  sudo python mqtt-pub.py
  Let’s get the receiver writing to Redis. Use 3 terminals. Verify on Browser
  sudo python get-redis-value.py  Flask web server to show values
  sudo python mqtt-sub.py  Puts message into Redis
  sudo python mqtt-pub.py  Publishes messages

## Slide 39: Lab 4: MQTT – End-to-end
Transfer the photoresistor readings from the Raspberry Pi
Keep the “Flask” and “Sub” terminals open. Don’t need the “Pub” one
IMPORTANT: Disable McAfee firewall if tethering
Open a terminal in Raspberry Pi and verify MQTT is working:
  mosquitto_pub -h your_laptop_IP -t test -m “The Pi says Hi!”
  sudo python rpi-pub.py  Edit the IP of your laptop first
  Can you see the message in the “sub” terminal? If so, you can run
  sudo python photo-pub.py  Edit the IP of your laptop first
  Refresh your browser. Does the value change?
  Check out the diagram of the services you need running for end-to-end
Notes: There are more and better examples on how to do stuff in the Paho official repo:
https://github.com/eclipse/paho.mqtt.python/tree/master/examples

## Slide 40: Lab 4: MQTT – End-to-end
If the Vagrant install was successful you can just run “photo-pub.py” in RPi
Open 2 terminals for the VM and run “photo-sub.py” and “get-redis-value.py”
  IMPORTANT: Don’t forget to enable your firewall again 
Rasberry Pi
photo-pub.py
Mosquitto
Service
Flask
get-redis-value.py
Redis
Service
Python
photo-sub.py
LAPTOP
Notes: There are more and better examples on how to do stuff in the Paho official repo:
https://github.com/eclipse/paho.mqtt.python/tree/master/examples

## Slide 41: From Prototype to Product

## Slide 42: Considerations
Power
  Relevant if the project needs mobility
  Some MCU have power saving\, disable WiFi
Security
  Much larger surface attach
    Including physical security
PCB vs Cabling
  Print commercially if multiple required
  Or do it at home
Casing and assembly

## Slide 43: Challenges from Falcon-Eye Project
Unstable cabling, run out of ports
No power to run outdoors

## Slide 44: Interesting Projects
Digital nose
  https://hackaday.io/project/16809-electronic-nose-to-detect-fruit-ripening
Ardusat or high altitude balloon or rocket data logger
  https://www.instructables.com/id/The-Ultimate-High-Altitude-Weather-Balloon-Data-Lo/
Duckietown (Autonomous cars by MIT)
  http://duckietown.mit.edu/
Mini plotter, laser engraver, 3D printer from old DVD drives
  https://www.instructables.com/id/How-to-Make-GRBL-CNC-V3-Shield-Based-Mini-CNC-Mach-1/
Self-balancing robot
  https://www.instructables.com/id/Self-Balancing-Robot/
Automated farming
  https://www.instructables.com/id/Automated-Greenhouse/
Notes: http://duckietown.mit.edu/

## Slide 45: Interesting Projects
NOAA Satellites or ISS signal receiver
  https://www.instructables.com/id/HackerBoxes-0003-Amateur-Radio-Arduino-Nano-Satell/
Synthesizer
  https://www.instructables.com/id/Auduino-Lo-Fi-Arduino-Synthesizer/
Seismometer
  https://www.instructables.com/id/Slinky-Seismometer/
Smart mirror
  https://hackaday.io/project/13466-raspberry-pi-smart-mirror
Home Automation
Robotic Arms (LittleArm, MeArm, …), rovers (line followers, obstacle avoidance, …)
Rubik cube solver
Notes: http://duckietown.mit.edu/

## Slide 46: Interesting Sites
Libelium
http://www.libelium.com/resources/top_50_iot_sensor_applications_ranking/
Instructables – Technology
http://www.instructables.com/tag/type-id/category-technology/
Hackster
https://www.hackster.io/projects?by=featured
Hackaday
https://hackaday.io/

## Slide 47: Homework

## Slide 48: Homework
Play with rest of the sensor kit
  This is the link to Adeept’s repo for our kit
  https://github.com/adeept/Starter_Kit_Python_Code_for_RPi
  Or you can download the whole pack here including PDF, diagrams, etc
  https://www.adrive.com/public/fG3Bf6/Adeept_Sensor_Kit_for_RPi.zip